## Slide 1: Sulfur-Iodine Thermochemical Rxn.
1. 2H2O(l) + SO2(g) + I2(l)→ H2SO4(l) + 2HI(l) 120°C
Bunsen Reaction
2a. H2SO4(l) → H2O(g) + SO3(g) ~850°C
2b. SO3(g) → SO2(g) + 0.5O2(g) ~500°C
3. 2HI (g) → I2(l) + H2(g) ~400°C

## Slide 4
Reactive Distillation
Equilibrium of reversible reaction highly temperature dependent
A + B  C + D
Using L’Chatlier’s Principle:
A + B  C + D
Heating mixture and extracting product will push reaction to right

## Slide 5: Vacuum Distillation
Each stage considered for the sulfur process (DOE) 
Low pressures (compared to the bunsen reactor) allows for high distillation
Note materials consideration
http://www.hydrogen.energy.gov/pdfs/review05/pd27_pickard.pdf

## Slide 6: Materials
Corrosive environment – H2SO4 , HI, H3PO4
High temperature
Closed system – three part reaction
Iodine section may generate residual solids

## Slide 7
Incoloy 800H:
Nickel-iron-chromium alloy, high strength, resistant to oxidation and carburization, temperatures above 1100°F
Pt, Au, SiC coating
Very unreactive, ceramics and other polymer coatings a consideration
Pt, Cu, Fe2O3
Catalysts, Cu and Fe2O3 cheap
Hastelloy C-276 (B-2)
Nickel-moly-chromium superalloy with resistance to corrosion and oxidation
Saramet
“Sulphuric acid resistant alloy metal”; due to high Si content – a.k.a. Si steels, with chromium and nickel balance

## Slide 8: Against other methods
Steam reforming – CH4 + H2O → CO + 3 H2
CO + H2O → CO2 + H2
Doesn’t cut out carbon emission
High or low temp electrolysis: H2O → O2 + H2
Needs extremely high temperatures for efficiencies ~45%
Others - methanol:
CO2 + 3H2 → CH3OH + H20
- dimethyl ether CH3OCH3
- Ammonia NH3

## Slide 9: DOE Hydrogen Program
2002 – 2008 (report in 2005 states 25% progress towards objectives)
Funding – $4.2M
Sandia Labs – H2SO4 reactor
CEA (Commissariat à l'énergie atomique) – Bunsen reactor
General Atomics (Japan) – Iodine Reactor/H2 extractor

## Slide 10: Very High Temperature Reactor (VHTR)
Current R&D – DRAGON, Peach Bottom
ONRL – NGNP design: graphite moderated
Metal-cooled fast reactors
Gas-cooled reactors: pebble bed
Numerous other designs, narrowed down by the DOE in the past two years
Deployment anticipated 2025
Varied fuel types and coatings – if outlet 900°C, fuel needs 1300°C
“To produce hydrogen economically, a reactor must operate at extremely high temperatures. Thus the VHTR has been selected for future hydrogen production plants. ‘The VHTR has the highest priority among the U.S. reactor concepts,’ [Bill] Corwin says, ‘because it fits into the President's plan for the hydrogen economy.’”
-”Can the Next Generation Take the Heat?” ORNL Review. http://www.ornl.gov/info/ornlreview/v37_1_04/article_02.shtml. 30 Nov 2010.

## Slide 11: Boiling Water Reactor (BWR)
Constrained by coolant
Low fuel temperature (compare PWR)
Larger pressure vessel – higher cost
PWRs: ~10% higher performance, increased temperature, but also has a ceiling

## Slide 12: Pebble Bed Reactor
Helium coolant: low density – collisions minimized
High flow for low specific heat capacity
Significant lethargy – slow neutrons (though graphite requires more collisions)
300,000 pebbles, 350 discarded daily
Involved fuel handling process

## Slide 13: Sodium-Cooled Fast Reactor (SFR)
Closed fuel cycle
Two lines of flow – HX between Pb and H2O
Fertile uranium, plutonium, and other actinides
Operates near ambient pressure
Difficulties with VHTR: Na melting point – 98°C
(At ambient pressure) Na boiling point – 883°C
Na highly reactive and corrosive

## Slide 14: Sodium-Cooled Fast Reactor

## Slide 15: Lead-Cooled Fast Reactor (LFR)
Lead/Bismuth coolant
Very similar to SFR – closed system liquid metal
Replaceable fuel module, designed to run 15-20 years
Designed to meet the needs of a small grid
Following design features U-Tube HX
Another Gen. IV design replaces liquid metal with helium, maintaining similar design but with varied HX

## Slide 16: Lead-Cooled Fast Reactor

## Slide 17: Advantages
Only liquid and vapor for fluid cycle
Sulfur and iodine components remain in system, H2 and O2 distilled out
Chemicals relatively cheap (HBr out of consideration)
Existing R&D – actualization is not too far off
Functional with intermittent renewables or unused heat of gen. IV reactors
No carbon footprint
Ƞ ~ 50%, beats HT electrolysis

## Slide 18: Disadvantages
Three components, cumbersome setup
Full cycle has not been perfected
Corrosive intermediates (HI, H2SO4, H3PO4)
High materials cost
Much R&D still necessary
Must wait on nuclear technology to advance – subject to public opinion, economy, legislature
Large scale necessary for satisfactory efficiencies (investment)

## Slide 19: References
“Boiling Water Reactors”. Nuclear Regulatory Commission. Oct 1 2008. <http://www.nrc.gov/reactors/bwrs.html>. 30 Nov 2010.
“Can The Next Generation Take The Heat?” Oak Ridge National Lab Review. Volume 37, Number 1, 2004. <http://www.ornl.gov/info/ornlreview/v37_1_04/article_02.shtml>. 30 Nov 2010.
Mashue, Timothy; Folger, H. S. “Reactive Distillation”. University of Michigan. 1998. <http://www.engin.umich.edu/~cre/web_mod/distill/>. 10 Nov 2010.
Mathias, Paul M.; Brown, L. C. “Thermodynamics of the Sulfur-Iodine Cycle for Thermochemical Hydrogen Production”. Society of Chemical Engineers, 68th annual meeting. 23 Mar 2003. <http://www.aspentech.com/publication_files/TP51.pdf>. 30 Nov 2010.
“Modular Pebble Bed Reactor”. MIT Department of Nuclear Science and Engineering. <http://web.mit.edu/pebble-bed/>. 30 Nov 2010.
Ogawa, Masuro; Lensa, W. v. “Very High Temperature Gas Cooled Reactor (VHTR)”. Generation IV R&D Scope Meeting. 25 Jun 2002. <http://gif.inel.gov/roadmap/pdfs/p_grns_june_25-27_presentation_gp32-00.pdf>. 30 Nov 2010.
Pickard, Paul. “2005 Hydrogen Program Review: Sulfur-Iodine Thermochemical Cycle”. Sandia National Labs; U.S. Department of Energy. May 25 2005. <http://www.hydrogen.energy.gov/pdfs/review05/pd27_pickard.pdf>. 30 Nov 2010.
Ragheb, Magdi. “HIGH TEMPERATURE WATER ELECTROLYSIS FOR HYDROGEN PRODUCTION”. University of Illinois – Champaign-Urbana. 19 Oct 2010. <https://netfiles.uiuc.edu/mragheb/www/NPRE%20498ES%20Energy%20Storage%20Systems/High%20Temperature%20Water%20Electrolysis%20for%20Hydrogen%20Production.pdf>. 30 Nov 2010.
Sponseller, Mike. “Lead-Cooled Fast Reactor (LFR)”. Idaho National Laboratory. <http://www.inl.gov/research/lead-cooled-fast-reactor/>. 30 Nov 2010.
Sponseller, Mike. “Sodium-Cooled Fast Reactor (SFR)”. Idaho National Laboratory. <http://www.inl.gov/research/sodium-cooled-fast-reactor/>. 30 Nov 2010.