## Slide 1
Renewable sources, nuclear power, and energy storage alternatives to reduce UIUC Campus CO2 emissions
Roberto Fairhurst Agosta
ref3@illinois.edu
NPRE 498 - Energy Storage - Spring 2021
University of Illinois at Urbana-Champaign

## Slide 2
Objectives
Propose electricity generation alternatives for decreasing CO2 emissions on UIUC campus.
  Objective aligned with Illinois Climate Action Plan (iCAP) objectives.
Understand the components of UIUC campus grid.
Determine current CO2 emissions in two representative months of the year.
Calculate CO2 emissions for different scenarios, including:
  Increase in wind generation capacity.
  Increase in solar generation capacity.
  Addition of a nuclear reactor to UIUC campus grid.
  Compare different electricity storage alternatives.

## Slide 3
iCAP [1]
American College and University Presidents’ Climate Commitment (2008)
Become carbon neutral as soon as possible, no later than 2050.
Development of the iCAP (2010)
Comprehensive roadmap toward a sustainable campus.
iCAP list of goals, objectives, and potential strategies for several topical areas:
  Energy Conservation and Building Standards
  Energy generation, Purchasing, and Distribution
  Transportation
  Water and Stormwater usage
  Purchasing, Waste, and Recycling (Zero Waste)
  Agriculture, Land Use, Food, and Sequestration

## Slide 4
UIUC Campus Grid [2]
Figure. FY19 Electricity generation distribution.

## Slide 5
ABBOTT Power Plant [3-4]
Built in 1941.
Supplies 70-75% of the campus energy demand.
Types of energy sources:
  Two gas turbines (natural gas or fuel oil)
  Three gas-fired boilers (natural gas or fuel oil)
  Three coal-fired boilers
Cogeneration facility: steam and electricity
  High-pressure steam spins a turbine to drive a generator and produce electricity.
  Low-pressure exhaust steam for space heating, water heating, and space cooling.
  Electrical capacity 85 MW.
Free tours.

## Slide 6
Rail Splitter Wind Farm [5-6]
Operation began in 2009.
Located in Tazewell and Logan Counties.
Power output: 100.5 MW.
67 turbines of 1.5 MW.
Power purchase agreement:
  November 2016 - October 2026
  8.6% of the total wind generation

## Slide 7
Solar Farm 1.0 [7-8]
Operation began in 2015.
Power output: 4.68 MWac.
Total modules: 18,867.
Land usage: 20.8 acres.
Power purchase agreement: 2015-2025.
Solar Farm 2.0: 12.32 MWdc, 54 acres.

## Slide 8
Small Modular Reactors and Microreactors [9-10]
UIUC Grid demand < 80 MW.
Limited on-site preparation requirements.
Factory-fabricated components.
Components shipped out to generation site.
Black starts and islanding operation mode.
Passive safety systems, minimizing electrical parts.

## Slide 9
Li-ion Batteries [11-15]
Charge-Discharge Efficiency: 80-90%
Rechargeable battery
First prototype developed in 1985
High energy density and low self-discharge
Can cause explosions and fires
Capacity fading over hundreds to thousands of cycles
Applications:
  Portable Power Packs: Laptops and cellphones
  Electric Vehicles (EVs)
  Uninterruptible Power Supply (UPS): computers, communication technology, medical technology
  Solar power storage
World largest Li-ion: 150 MW

## Slide 10
Electrolysis [16]
Commercial use since 1890.
Most common technologies:
  Alkaline-based
  Proton exchange membrane (PEM)
  Solid Oxide (SOEC)
Low temperature electrolysis (LTE)
High temperature electrolysis (HTE)
Equation:
𝚫H = 𝚫G + T𝚫S
𝚫H: Specific total energy
𝚫G: Specific electrical energy
T𝚫S: Specific thermal energy

## Slide 11
Scenario 0 - Business as usual
We will focus in a summer month (June) and a winter month (January)
Data available from F&S per request [17]
Abbott: 0.26 tCO2/MW(th)h [1-2]
Imports: 0.825 tCO2/MWh [1-2]
Wind
Solar
Abbott
Import
Demand

## Slide 12
Scenario 0 - Results
103 MT CO2 | Abbott | Imports | Total
Winter | 6.6 | 8.5 | 15.1
Summer | 4.8 | 16.7 | 21.5

## Slide 13
Scenario 1
Dispatch model
  Wind and Solar
  Storage
  Abbott
  Import
Increase in Wind and Solar capacity
Net Demand (ND) = Demand - Wind - Solar
Necessity for storage mechanisms

## Slide 14
Scenario 1 - Results
Capacity increase by 10, Wind: 100.5 MW, Solar: 46.8 MW

## Slide 15
Scenario 1 - Results

## Slide 16
Scenario 2
Dispatch model
  Wind and Solar
  Nuclear Reactor
  Storage
  Abbott
  Import
Increase in Wind and Solar capacity
Increase in Reactor Capacity
Net Demand (ND) = Demand - Wind - Solar - Reactor
Necessity for storage mechanisms
HTE at 3.5 MPa

## Slide 17
Scenario 2 (2)
PE = 𝜼 𝛽 PTH
PEH2 = 𝜼 𝛄 (1 - 𝛽) PTH
PTH2 = (1 - 𝛄) (1 - 𝛽) PTH
𝜼 = 𝜼(To)
𝜼: conversion efficiency
To: reactor outlet temperature
𝛽 = PE/𝜼 / (PE/𝜼 + PTH2/(1-𝛄))
𝛄 =PEH2/𝜼 / (PEH2/𝜼 + PTH2)
 | 𝛄 | PEH2 | PTH2
LTE | 1 | ≠ 0 | 0
HTE | (0-1) | ≠ 0 | ≠ 0

## Slide 18
Scenario 2 - Results
Capacity increase by 10, Wind: 100.5 MW, Solar: 46.8 MW, Reactor: 10 MWth

## Slide 19
Scenario 2 - Results - Summer

## Slide 20
Scenario 2 - Results - Winter

## Slide 21
Conclusions
UIUC campus grid is a good example of a diverse microgrid.
Winter CO2 emissions are lower to Summer CO2 emissions.
  Total demand is lower as well.
  Future work may include the same analysis using February dataset.
Decreasing the imported electricity considerably reduces CO2 emissions.
Abbott steam production may limit max electric capacity.
Increase in renewables capacity linearly decreases CO2 emissions if no storage mechanism is needed.
In Scenario 1, increasing wind and solar capacity requires:
  Battery of around 70 MW.
  Hydrogen plant that can support 1400 kg/h.
Larger reactor capacities reduce further the CO2 emissions.
Larger reactor outlet temperature increases storage efficiency.
HTE-H2 production is limited by the size of the reactor, secondary method required.
Li-ion is the most efficient storage mechanism.

## Slide 22
Acknowledgements
I would like to thank Sam Dotson and Lucas Woodrich for putting together most of the data that was used in this work.
This research was performed using funding received from the DOE Office of Nuclear Energy’s University Program (Project 20-19693, DE-NE0008972) ’Evaluation of micro-reactor requirements and performance in an existing well-characterized micro-grid’.

## Slide 23
References
[1] - https://icap.sustainability.illinois.edu/files/project/2634/2015iCAPweb.pdf
[2] - https://icap.sustainability.illinois.edu/files/project/5293/iCAP-2020-FINAL-WEB.pdf
[3] - https://fs.illinois.edu/services/utilities-energy/production/abbott-power-plant
[4] - https://fs.illinois.edu/docs/default-source/utilities-energy/abbottbrofinal.pdf?sfvrsn=90b1f9ea_4
[5] - https://icap.sustainability.illinois.edu/files/project/2235/RailSplitter-Wind%20Farm-9.6.16.pdf
[6] - https://fs.illinois.edu/services/utilities-energy/production/renewable-energy
[7] - https://fs.illinois.edu/docs/default-source/utilities-energy/solar-farm-project-fact-sheet_with-faqs_104171bbba4c36b8160c2ad00ff2500358aeb.pdf?sfvrsn=813ac4ea_0
[8] - https://icap.sustainability.illinois.edu/project/solar-farm-20
[9] - https://www.energy.gov/ne/downloads/ultimate-fast-facts-guide-nuclear-energy
[10] - https://twitter.com/govnuclear/status/1282822874865242117

## Slide 24
References (2)
[11] - http://large.stanford.edu/courses/2010/ph240/sun1/
[12] - https://www.ornl.gov/news/new-class-cobalt-free-cathodes-could-enhance-energy-density-next-gen-lithium-ion-batteries
[13] - https://relionbattery.com/blog/the-seven-top-uses-for-rechargeable-lithium-ion-batteries
[14] - https://en.wikipedia.org/wiki/Lithium-ion_battery#Battery_life
[15] - https://www.tesla.com/videos/powerpack-hornsdale?redirect=no
[16] - Fairhurst-Agosta R. MULTI-PHYSICS AND TECHNICAL ANALYSIS OF HIGH-TEMPERATURE GAS-COOLED REACTORS FOR HYDROGEN PRODUCTION. MS Thesis. University of Illinois at Urbana-Champaign. 2020. https://www.ideals.illinois.edu/handle/2142/109439
[17] - UIUC F&S. Private Communications. 2019. 2020.

## Slide 25
Thank you! Questions?